## Slide 1: CS 31006: Computer Networks – History and Protocol Stack

## Slide 2: Circuit Switching – the Beginning
The concept of how telephone switching works – creates a dedicated communication links between two communication nodes (telephones)
In January 1878, the first telephone switch went into operation in New Haven Connecticut.

## Slide 3: Circuit Switching
Source: http://comp380group4project1.web.unc.edu/technical-discussion/circuit-switching/

## Slide 4: Problem with Circuit Switching for Data Communication
Data traffic is bursty – uses an on-off pattern for data communication.

## Slide 5: Packet Switching
Decide data boundary from the communication of one user – data packets
Packet Multiplexing

## Slide 6: The First Packet Switching Network
Robert Taylor was promoted to the head of the information processing office at Defense Advanced Research Projects Agency (DARPA) in June 1966. He intended to realize Licklider's ideas of an interconnected networking system. Bringing in Larry Roberts from MIT, he initiated a project to build such a network. The first ARPANET link was established between the University of California, Los Angeles (UCLA) and the Stanford Research Institute at 22:30 hours on October 29, 1969.
Kleinrock said in an interview: "We typed the L and we asked on the phone,
  "Do you see the L?"
  "Yes, we see the L," came the response.
  We typed the O, and we asked, "Do you see the O."
  "Yes, we see the O."
  Then we typed the G, and the system crashed ...
Yet a revolution had begun"
By December 5, 1969, a 4-node network was connected by adding the University of Utah and the University of California, Santa Barbara.
Source: Wikipedia

## Slide 7: ARPANET – The First Packet Switching Network

## Slide 8: History of Computer Networks
https://www.youtube.com/watch?v=9hIQjrMHTv4
https://www.internetsociety.org/internet/history-internet

## Slide 9: TCP/IP Protocol Stack
Physical
Data Link
Network
Transport
Application
Physical
Data Link
Network
Transport
Application
Physical
Data Link
Physical
Data Link
Network
Physical
Data Link

## Slide 10: Transport Layer Services
Connection oriented communication
  Create a logical connection between your machine and Google server
Process to process Connection
Identify processes using port number

## Slide 11: Transport Layer Services
Connection oriented communication
  Create a logical connection between your machine and Google server
Ordered delivery of data packets
Reliability
Flow control
Congestion avoidance

## Slide 12: Network (Internet) Layer Services
Connectionless communication - construct messages (datagrams) from packets and route them to the next hop
  Why do transport layer packets need to be converted to datagrams at every hop?
Host addressing - use IP addresses to uniquely identify a host in the network
Datagram routing - decide the path to route every datagram from the network graph

## Slide 13: Data Link Layer Services
Encapsulation of network layer data packets into frames
Frame synchronization
Error control
Flow control
  Why do we need flow control at the link layer?
Channel access / medium access, Physical addressing

## Slide 14: Data Link Layer
Medium Access Control (MAC)
Logical Link Control (LLC)
Error control and flow control
Channel access and physical layer
addressing

## Slide 15: Addressing a Host in the Network
Every host has two addresses –
  Logical address (IP address) – used to find out the path towards a host
  Physical address (MAC address) - uniquely identify a host in the Internet
Logical address – Dr. Sandip Chakraborty, Room-311, Department of Computer Science and Engineering, IIT Kharagpur, Kharagpur - 721302, West Bengal, India
Physical address – My Aadhar number (XXXX XXXX XXXX)

## Slide 16: Addressing a Host in the Network
Every host has two addresses –
  Logical address (IP address) – used to find out the path towards a host
  Physical address (MAC address) - uniquely identify a host in the Internet
Logical address (32 bit IP address) – 172.16.32.64
Physical address (64 bit MAC address) – 00:00:00:14:22:01:2C:4D

## Slide 17: Protocol Stack Implementation in a Host
Software, Kernel
Firmware, Device Driver
Hardware
Physical
Data Link
Network
Transport
Application

## Slide 18: How Application Data Passes Through Different Layers
Physical
Data Link
Network
Transport
Application
HTTP Data
HTTP Header
HTTP Data
HTTP Header
TCP Header
HTTP Data
HTTP Header
TCP Header
IP Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
PHY Header
PHY Trailer

## Slide 19: How do you access a page at www.google.com?
Application Layer: Use DNS to get the IP address of the Google server - DNS returns 74.125.224.72
Application Layer: Construct an HTTP GET Request – GET 74.125.224.72/index.html HTTP/1.1 Construct an HTTP packet and forward it to the transport layer

## Slide 20: How do you access a page at www.google.com?
Transport Layer: Construct the transport layer packet (TCP packet)
  Source port: 3324 (port address corresponding to your browser tab)
  Destination port: 80 (port for a HTTP server)

## Slide 21: How do you access a page at www.google.com?
Network Layer: Construct the network layer packet (IP packet)
  Source IP: 172.16.22.121 (IP of your machine)
  Destination IP: Next hop IP for 74.125.224.72 (use the routing procedure to get this IP)

## Slide 22: How do you access a page at www.google.com?
Network Layer: Use the routing procedure to find out the next hop IP to reach the Google server at 74.125.224.72. Let this IP be 172.16.28.192
172.16.28.192
172.16.22.121
74.125.224.72

## Slide 23: How do you access a page at www.google.com?
Data Link Layer: Construct the data link layer frame from the IP datagram.
  How do we get destination MAC address? We need the MAC address corresponding to 172.16.28.192
172.16.28.192
172.16.22.121
Gateway
Local Area Network (LAN)

## Slide 24: How do you access a page at www.google.com?
Data Link Layer: Use ARP protocol to get the MAC address corresponding to 172.16.28.192
172.16.28.192
172.16.22.121
Gateway
Local Area Network (LAN)

## Slide 25: In Summary
Physical
Data Link
Network
Transport
Application
HTTP Data
HTTP Header
HTTP Data
HTTP Header
TCP Header
HTTP Data
HTTP Header
TCP Header
IP Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
PHY Header
PHY Trailer