## Slide 1: CS 31006: Computer Networks – Application Layer

## Slide 2: Protocol Stack Implementation in a Host
Software, Kernel
Firmware, Device Driver
Hardware
Physical
Data Link
Network
Transport
Application

## Slide 3: How Application Data Passes Through Different Layers
Physical
Data Link
Network
Transport
Application
HTTP Data
HTTP Header
HTTP Data
HTTP Header
TCP Header
HTTP Data
HTTP Header
TCP Header
IP Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
PHY Header
PHY Trailer

## Slide 4: Application Layer Interfacing
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Network
Transport
Application - 1
Data Link
Application - 2
Application - 3
Application - 4

## Slide 5: Application Layer Interfacing
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Network
Transport
Name Service
(DNS)
Data Link
Web
(HTTP)
Email
(SMTP, POP, IMAP)
File Transfer
(FTP)

## Slide 6: Domain Name System (DNS)
Assign Unique names to an IP address (machine interface)
ARPANET – a file hosts.txt listed all the computer names and their IP addresses.
Resolve the host name conflicts over the Internet – a naming hierarchy needs to be managed
  Rooted at an organization Internet Corporation for Assigned Names and Numbers (ICANN)

## Slide 7: The DNS Name Space
The top level domains are run by registrars appointed by ICANN
Name registrar for India (.in domain): registry.in (National Internet Exchange of India – NIXI)
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 8: registry.in

## Slide 9: Registrars Under registry.in

## Slide 10: Elements of DNS (RFC 1034)
The Domain Name Space and Resource Records: Specifications for a tree-structured namespace and data associated with names.
Name Servers: Server programs which hold information about the domain tree’s structure and set information
  A particular name server has complete information about a subset of the domain space
  Name servers know the parts of the domain tree for which they have complete information -- a name server is said to be an AUTHORITY for this parts of the namespace

## Slide 11: Name Servers
Divide registries into non-overlapping zones – every zone has a name server
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 12: Elements of DNS (RFC 1034)
The Domain Name Space and Resource Records: Specifications for a tree-structured namespace and data associated with names.
Name Servers: Server programs which hold information about the domain tree’s structure and set information
  A particular name server has complete information about a subset of the domain space
  Name servers know the parts of the domain tree for which they have complete information -- a name server is said to be an AUTHORITY for this parts of the namespace
Resolvers: Program that extracts information from name servers in response to client requests

## Slide 13: Domain Resource Records
Every domain has a set of resource records associated with it – DNS database

## Slide 14: Domain Resource Records
Domain_name: Domain to which the record applies.
Time_to_live: Time for which this record is active – volatile records may be assigned a small value
Class: Normally IN – Internet resources
Type: What type of record it is
Value: Value of the record (IP address for A record type)

## Slide 15: Domain Resource Records
A Type Records: cse.iitkgp.ac.in 86400 IN A 203.110.245.250
CNAME Type Records: iitkgp.ac.in 86400 IN CNAME www.iitkgp.ac.in
PTR Type Records: www.iitkgp.ernet.in 86400 IN PTR www.iitkgp.ac.in

## Slide 16: Sample DNS Database
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 17: Name Resolution – Looking Up for the Names
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 18: DNS Packet Structure

## Slide 19: Name Resolution (nslookup)
One of the name servers for IITKGP

## Slide 20: Name Resolution (dig)
An authoritative record is one that comes from the authority that manages the record, and thus is always correct
UDP Message for 4096 bytes

## Slide 21: Why DNS Uses UDP
UDP is much faster. TCP requires handshake time. DNR uses a cascading approach for name resolution. With TCP, for every message, a connection setup is required.
DNS requests and responses are generally very small, and fits well within one UDP segment.
UDP is not reliable. In DNS, reliability is ensured at the application layer. After timeout, the DNS client sends back the requests. After few consecutive timeouts (can be set at the client), the request is aborted with an error.

## Slide 22: Application Layer Interfacing
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Network
Transport
Name Service
(DNS)
Data Link
Web
(HTTP)
Email
(SMTP, POP, IMAP)
File Transfer
(FTP)

## Slide 23: The Web – Hypertext Transfer Protocol (HTTP)
Hypertext - A way to represent web content (text along with formatting)
Hypertext Markup Language (HTML) - A scripting language to specify web data along with simple formatting (bold, italics, new line).
  A way to convert text based information to graphics based information
Today’s era: Many graphics, scripts and other information are embedded inside HTML – CSS, JavaScript etc.

## Slide 24: Differences between HTML Versions
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 25: A History of the Web
1989 (CERN – European Center for Nuclear Research) – help large teams to collaborate using a constantly changing collection of reports, blueprints, drawings, photos and other documents
  The proposal came from Tim Berners-Lee
  A public demonstration at Hypertext ‘91 conference
1993 – The first graphical browser (Mosaic) developed by Marc Andreessen, University of Illinois
  Andreessen formed the company Netscape Communications Corp
  Microsoft developed Internet Explorer – “browser war” between Internet Explorer and Netscape Navigator
1994 – CERN and MIT signed an agreement to setup World Wide Web Consortium (W3C)

## Slide 26: The Web – Architectural Overview
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 27: HTTP – The Client Side
Three questions to be answered for accessing a web page
  What is the page called? (courses.html)
  Where is the page located? (cse.iitkgp.ac.in/~sandipc/)
  How can the page be accessed? (http://)
Uniform Resource Locator (URL): Each page is assigned a URL that effectively serves the page’s worldwide name
URL have three components:
  The protocol
  The qualified name of the machine one which the page is located
  The path uniquely indicating the specific page
http://cse.iitkgp.ac.in/~sandipc/courses.html

## Slide 28: The Steps When You Click http://cse.iitkgp.ac.in/~sandipc/courses.html
The browser determines the URL
The browser asks DNS for the IP address of the server cse.iitkgp.ac.in
DNS replies with 203.110.245.250
The browser makes a TCP connection to 203.110.245.250 on port 80, the well known port for the HTTP protocol
It sends over an HTTP request asking for the page /courses.html
The cse.iitkgp.ac.in server sends the page as an HTTP response, for example by sending the file /courses.html
If the page includes URLS that are needed for display, the browser fetches the other URLs using the same process.

## Slide 29: The Steps When You Click http://cse.iitkgp.ac.in/~sandipc/courses.html

## Slide 30: The Steps When You Click http://cse.iitkgp.ac.in/~sandipc/courses.html
The browser displays the page courses.html
The TCP connections are released if there are no other requests to the same server for a short period.

## Slide 31: Uniform Resource Identifier (URI)
Generalization of the URLs – specifies the pages only or partially refers the pages without complete locations
/images/iit_kgp.png – may become URL https://cse.iitd.ac.in/images/iit_kgp.png if accessed from cse.iitd.ac.in

## Slide 32: HTTP – The Server Side
Accept a TCP connection from a client (a browser).
Get the path to the page, which is the name of the file requested.
Get the file (from disk).
Sends the content of the file to the client.
Release (close) the TCP connection.

## Slide 33: Multi-Threaded Server
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell
Serves multiple client requests simultaneously

## Slide 34: Connections
HTTP uses TCP to set up a connection between the server and the client. In general, HTTP server runs at port 80 (default port) or 8080 (alternate port).
HTTP 1.0 – After the connections were established, a single request was sent over and a single response was sent back. Then the TCP connections are released.
  Create separate connections for every content in the web-page. Overhead is high.
Persistent Connection (HTTP 1.1) – send additional requests and additional responses in a single TCP connection (connection reuse).
  It is also possible to pipeline requests.

## Slide 35: Connections
HTTP 1.0
HTTP 1.1 – Persistent Connections
HTTP 1.1 – Persistent Connections (Pipelined)
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell
Persistent Connections: Set at keep-alive information in the HTTP header (HTTP 1.0)
HTTP 1.1 – All connections are by default persistent

## Slide 36: HTTP Request Methods
Specifies what a HTTP Request will do
GET filename HTTP/1.1

## Slide 37: HTTP Request Header Fields (Partial List)

## Slide 38: HTTP Response
Specifies the status of the request message.

## Slide 39: HTTP Response Header Fields (Partial List)

## Slide 40: HTTP Caching
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 41: Dynamic Web Applications
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 42: Cookies
HTTP is by default a stateless protocol
  Every Response corresponds to the previous Request only, it does not remember any state information, such as last page accessed
Use Cookies to store the state information. Client forwards the additional information along with the Request message by reading the cookie.

## Slide 43: HTTP Proxy
Intercepts the TCP connections to process the HTTP data.
HTTP Proxy

## Slide 44: Application Layer Interfacing
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Network
Transport
Name Service
(DNS)
Data Link
Web
(HTTP)
Email
(SMTP, POP, IMAP)
File Transfer
(FTP)

## Slide 45: Electronic Mails – Architecture and Services
User Agent: Allow people to read and send emails.
Message Transfer Agents (main servers): Move the message from the source to the destination
sandipc@cse.iitkgp.ernet.in
sukumar@iitg.ernet.in
cse.iitkgp.ernet.in
iitg.ernet.in

## Slide 46: Message Transfer Agents
System processes run in the background on mail servers (always available).
Automatically move emails through the system from the originator to the recipient
Uses Simple Mail Transfer Protocol (SMTP) – RFC 821, RFC 5321
Implements mailing lists, an identical copy of message is delivered to everyone in the list (btech@iitkgp.ac.in)
Implements Mailboxes, to store all the emails received for a user

## Slide 47: Message Format (RFC 5322)
An envelope containing message header and message body

## Slide 48: The Internet Message Format (RFC 5322)
Header fields (for message transport):

## Slide 49: The Internet Message Format (RFC 5322)
Header fields (additional fields for message description):

## Slide 50: MIME – The Multipurpose Internet Mail Extension
ARPANET: email consisted exclusively of text messages written in English and expressed in ASCII
MIME: Use multi-language and multimedia contents (audio, image etc.) inside an email.
Additional message headers for MIME:

## Slide 51: Message Transfer
Uses SMTP Protocol
Email is delivered by having the sending computer establishing TCP connection to port 25 of the receiving computer.
SMTP Server
(Port 25)
SMTP Client (Port ANY)
SMTP Server
(Port 25)
SMTP Client (Port ANY)
UA – SMTP Client
Port ANY
TCP
TCP
sandipc@cse.iitkgp.ernet.in
cse.iitkgp.ernet.in
iitg.ernet.in
SMTP
SMTP

## Slide 52: Message Transfer (SMTP)
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 53: Final Delivery
Pull type protocol – UA at the receiver side pulls the emails from mail server after login.
Post Office Protocol, Version 3 (POP3) – an earlier protocol for email delivery
Internet Message Access Protocol, Version 4 (IMAP v4) – RFC 3501
  The email server runs an IMAP server at port 143
  The user agent runs IMAP client
  The client connects to the server and issues mail delivery commands

## Slide 54: IMAP (Version 4) Commands

## Slide 55: Application Layer Interfacing
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Network
Transport
Name Service
(DNS)
Data Link
Web
(HTTP)
Email
(SMTP, POP, IMAP)
File Transfer
(FTP)

## Slide 56: File Transfer Protocol (FTP)
Is built on a client-server model (RFC 959)
  The client requests for the file or send the file to the server
  The server responses with the file data or store the file at the file server
Works in two modes – Active and Passive
File Server
(FTP Server)
User
(FTP Client)
File Request
File Response Status
File Data

## Slide 57: Active and Passive Modes of File Transfer
FTP server uses two different ports:
Port 21 (Command or Control Port): For command message transfer
Port 20 or Client assigned (Data Port): For data transfer
Image Source: http://henrydu.com/blog/how-to/ftp-active-mode-vs-passive-mode-106.html

## Slide 58: Why There are Two Channels – Command Channel and Data Channel
Specifically to avoid busy waiting, and keep the command channel lightweight.
You can always use a multiplexing between command/control and data, but FTP is used for large file transfer; if command channel is used for data transfer as well, the commands for other clients may experience a higher queuing delay while one client is being served.
The clients can continue sending and receiving control information while data transfer is being take place

## Slide 59: Why There are Two Modes in FTP?
Active Mode: Client informs the port number where it is listening, and the server initiates the TCP connection to that port (TCP server is running at the client side)
What If the client is behind a firewall and can not accept a connection?

## Slide 60: Why There are Two Modes in FTP?
Passive Mode: The server selects a random port, and the client initiates a TCP connection to that server port.
The server can serve multiple clients at different server data ports through different threads.
The clients always initiate the command and the data transfer.
Image Source: http://henrydu.com/blog/how-to/ftp-active-mode-vs-passive-mode-106.html

## Slide 61: FTP Data Transfer Modes
Stream mode: Data is sent as a continuous stream, relieving FTP from doing any processing. Rather, all processing is left up to TCP. No End-of-file indicator is needed, unless the data is divided into records.
Block mode: FTP breaks the data into several blocks (block header, byte count, and data field) and then passes it on to TCP.
Compressed mode: Data is compressed using a simple algorithm (usually run-length encoding).
Source: Wikipedia

## Slide 62: FTP Sample Commands and Response Codes

## Slide 63
Next, we’ll go for the Transport Layer ….